## Slide 1: Descriptive and inferential statistical methodologies have proven effective in creating a proactive ‘alarm’, accurately identifying Pump Failures with Horse Power (HP) and Pump Efficiency (PE) emerging as key variables of interest with deviations of 15 HP and > 3 % PE being our core signal thresholds.
Note: We’ve included a sample headline for you – you can feel free to use this or modify this as you see fit
Chart: Statistical Alarm Plot
Chart: Correlation Coefficient Stdev Data
| Horse Power | Volumetric Flow Meter 1 | Pump Efficiency | Volumetric Flow Meter 2 | Pump Speed (RPM) | Ambient Temperature | Pump Torque
Correlation Coefficient | 0.6901 | 0.64488 | 0.64355 | 0.62592 | 0.62456 | 0.60005 | 0.59726

## Slide 2: Descriptive Analysis has enabled us to clearly identify particular signature abnormalities showing clear signature changes in both Rolling Standard Deviation and Rolling Mean Datasets when observed over the respective failure period of interest.
Note: We’ve included a sample headline for you – you can feel free to use this or modify this as you see fit
Chart: DRT Rolling Stdev Plot
Chart: DRT Rolling Mean Plot

## Slide 3: Further segmentation of the data via binary means (Pump Failure = 0 or 1) illustrated through box plots show a clear signature difference between that of normal behaviour and that of Failure with Pump Torque, Pump Speed, and Ambient Temperature showing the 3 largest variances.

## Slide 4: Correlation analyses across datasets yield particularly interesting insights with Pump Torque and Pump Speed negatively correlated with Pump Failure in the Rolling Standard Deviation Data, whilst Pump Torque and Pump Speed show a subsequently strong positive correlation in the Rolling Mean Dataset.
Chart: Correlation Strength Associated with Pump Failure(Raw Data)
| Horse Power | Pump Speed (RPM) | Pump Torque | Ambient Temperature | Volumetric Flow Meter 1 | Pump Efficiency | Volumetric Flow Meter 2
Correlation Coefficient | 0.42184 | 0.26002 | 0.23319 | 0.20795 | -0.10251 | -0.10268 | -0.11211
Chart: Correlation Strength Associated with Pump Failure(Rolling Mean)
| Horse Power | Pump Speed (RPM) | Pump Torque | Ambient Temperature | Volumetric Flow Meter 1 | Pump Efficiency | Volumetric Flow Meter 2
Correlation Coefficient | 0.21805 | -0.18416 | -0.21594 | -0.30262 | -0.69243 | -0.69503 | -0.69773
Chart: Correlation Coefficient Stdev Data
| Horse Power | Volumetric Flow Meter 1 | Pump Efficiency | Volumetric Flow Meter 2 | Pump Speed (RPM) | Ambient Temperature | Pump Torque
Correlation Coefficient | 0.6901 | 0.64488 | 0.64355 | 0.62592 | 0.62456 | 0.60005 | 0.59726

## Slide 5: Lastly, analysis of the statistical significance of variables contributing towards Pump Failure reveal that with a R Squared of ~0.78, a linear model is a good fit for the data with both Rolling Mean and Rolling Standard Deviation datasets contributing key information to understand Pump Failure mechanics.
Variable | P-Value Significance
Horse Power | 3.55E-219
Volumetric Flow Meter 2 | 2.03E-174
Pump Efficiency | 2.59E-152
Pump Torque | 1.06E-102
Pump Speed (RPM) | 1.68E-19
Ambient Temperature | 4.21E-09
Volumetric Flow Meter 1 | 4.02E-07
Chart: Ranking of Variable Significance
| Horse Power | Volumetric Flow Meter 2 | Pump Efficiency | Pump Torque | Pump Speed (RPM) | Ambient Temperature | Volumetric Flow Meter 1
 | 3.5524e-219 | 2.033e-174 | 2.592e-152 | 1.0551e-102 | 1.683e-19 | 4.2052e-09 | 4.0155e-07